## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #23
Cache
Part II: Set/Fully Associative Cache

## Slide 2: Questions?
Scan and ask your questions here! (May be obscured in some slides)
Ask at
https://sets.netlify.app/module/676ca3a07d7f5ffc1741dc65
OR

## Slide 3: Lecture #23: Cache II: Set/Fully Associative Cache
Types of Cache Misses
Block Size Trade-off
Set Associative Cache
Fully Associative Cache
Block Replacement Policy
Additional Examples
Summary
Exploration

## Slide 4: 1. (Recall) Types of Cache Misses
Compulsory misses
  On the first access to a block; the block must be brought into the cache
  Also called cold start misses or first reference misses
Conflict misses
  Occur in the case of direct mapped cache or set associative cache, when several blocks are mapped to the same block/set
  Also called collision misses or interference misses
Capacity misses
  Occur when blocks are discarded from cache as cache cannot contain all blocks needed

## Slide 5: 2. Block Size Trade-off (1/2)
Larger block size:
  + Takes advantage of spatial locality
  – Larger miss penalty: Takes longer time to fill up the block
  – If block size is too big relative to cache size
   Too few cache blocks  miss rate will go up
Miss
Penalty
Block Size
Miss
Rate
Exploits Spatial Locality
Fewer blocks:
compromises
temporal locality
Block Size
Average
Access
Time
Block Size
Average Access Time
= Hit rate x Hit Time + (1-Hit rate) x Miss penalty

## Slide 6: 2. Block Size Trade-off (2/2)

## Slide 7: 3. Set Associative (SA) Cache
Compulsory misses
  On the first access to a block; the block must be brought into the cache
  Also called cold start misses or first reference misses
Conflict misses
  Occur in the case of direct mapped cache or set associative cache, when several blocks are mapped to the same block/set
  Also called collision misses or interference misses
Capacity misses
  Occur when blocks are discarded from cache as cache cannot contain all blocks needed
Solution:
Set Associative Cache

## Slide 8: 3. Set Associative Cache: Analogy
Many book titles start with “T”
 Too many conflicts!
Hmm… how about we give more slots per letter, 2 books start with “A”, 2 books start with “B”, …. etc?

## Slide 9: 3. Set Associative (SA) Cache
N-way Set Associative Cache
  A memory block can be placed in a fixed number (N) of locations in the cache, where N > 1
Key Idea:
  Cache consists of a number of sets:
    Each set contains N cache blocks
  Each memory block maps to a unique cache set
  Within the set, a memory block can be placed in any of the N cache blocks in the set

## Slide 10: 3. Set Associative Cache: Structure
An example of 2-way set associative cache
  Each set has two cache blocks
A memory block maps to a unique set
  In the set, the memory block can be placed in either of the cache blocks
   Need to search both to look for the memory block
2-way Set Associative Cache
00
01
10
11
Set Index
Data
Tag
Valid
Data
Tag
Valid
Set

## Slide 11: 3. Set Associative Cache: Mapping
Cache Block size = 2N bytes
Number of cache sets = 2M
Offset = N bits
Set Index = M bits
Tag = 32 – (N + M) bits
Cache Block size = 2N bytes
Memory Address
31
0
N-1
N
Block Number
Offset
N+M-1
31
0
N-1
N
Tag
Offset
Set Index
Cache Set Index
= (BlockNumber) modulo (NumberOfCacheSets)
Observation:
It is essentially unchanged from the direct-mapping formula

## Slide 12: 3. Set Associative Cache: Example
Memory
4GB
Memory Address
31
0
N-1
N
Block Number
Offset
1 Block
= 4 bytes
N+M-1
31
0
N-1
N
Tag
Offset
Set Index
Offset, N = 2 bits
Block Number = 32 – 2 = 30 bits
Check: Number of Blocks = 230
Number of Cache Blocks
= 4KB / 4bytes = 1024 = 210
4-way associative, number of sets
= 1024 / 4 = 256 = 28
Set Index, M = 8 bits
Cache Tag = 32 – 8 – 2 = 22 bits
Cache
4 KB

## Slide 13: 3. Set Associative Cache: Circuitry
Hit
Data
0
1
2
.
.
.
254
255
V
Tag
Data
0
1
2
.
.
.
254
255
V
Tag
Data
0
1
2
.
.
.
254
255
V
Tag
Data
0
1
2
.
.
.
254
255
V
Tag
Data
22
=
=
=
22
22
22
A
=
B
C
D
31 30 . . . 11 10 9 . . . 2 1 0
Tag
Idx
Ofst
4 x 1 Select
A
B
C
D
8
Set Index
22
Tag
32
4-way 4-KB cache: 1-word (4-byte) blocks
Note the simultaneous "search" on all tags of a set.

## Slide 14: 3. Advantage of Associativity (1/3)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Block Number (Not Address)
00
01
10
11
Cache Index
Example:
Given this memory access sequence: 0 4 0 4 0 4 0 4
Result:
Cold Miss = 2 (First two accesses)
Conflict Miss = 6 (The rest of the accesses)
Memory
Cache
Direct Mapped Cache
a block

## Slide 15: 3. Advantage of Associativity (2/3)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Block Number (Not Address)
00
01
Set Index
Example:
Given this memory access sequence: 0 4 0 4 0 4 0 4
Result:
Cold Miss = 2 (First two accesses)
Conflict Miss = None (as all of them are hits!)
Memory
Cache
2-way Set Associative Cache
a block

## Slide 16: 3. Advantage of Associativity (3/3)
Rule of Thumb:
A direct-mapped cache of size N has about the same miss rate
as a 2-way set associative cache of size N/2

## Slide 17: 3. SA Cache Example: Setup
Given:
  Memory access sequence: 4, 0, 8, 36, 0
  2-way set-associative cache with a total of four 8-byte blocks  total of 2 sets
  Indicate hit/miss for each access
4
31
0
2
3
Tag
Offset
Set Index
Offset, N = 3 bits
Block Number = 32 – 3 = 29 bits
2-way associative, number of sets= 2 = 21
Set Index, M = 1 bits
Cache Tag = 32 – 3 – 1 = 28 bits

## Slide 18: 3. SA Cache Example: Load #1
Load from 4 
Check: Both blocks in Set 0 are invalid [ Cold Miss ]
000000000000000000000000000
100
Tag
Offset
0
Index
 | Block 0 |  |  |  | Block 1 |  |  | 
Set Index | Valid | Tag | W0 | W1 | Valid | Tag | W0 | W1
0 | 0 |  |  |  | 0 |  |  | 
1 | 0 |  |  |  | 0 |  |  | 
4, 0 , 8, 36, 0
Result: Load from memory and place in Set 0 - Block 0
0
M[0]
1
M[4]
Miss

## Slide 19: 3. SA Cache Example: Load #2
 | Block 0 |  |  |  | Block 1 |  |  | 
Set Index | Valid | Tag | W0 | W1 | Valid | Tag | W0 | W1
0 | 1 | 0 | M[0] | M[4] | 0 |  |  | 
1 | 0 |  |  |  | 0 |  |  | 
Load from 0 
Result:
[Valid and Tags match] in Set 0-Block 0 [ Spatial Locality ]
000000000000000000000000000
000
Tag
Offset
0
Index
4, 0 , 8, 36, 0
Miss
Hit

## Slide 20: 3. SA Cache Example: Load #3
 | Block 0 |  |  |  | Block 1 |  |  | 
Set Index | Valid | Tag | W0 | W1 | Valid | Tag | W0 | W1
0 | 1 | 0 | M[0] | M[4] | 0 |  |  | 
1 | 0 |  |  |  | 0 |  |  | 
Load from 8 
Check: Both blocks in Set 1 are invalid [ Cold Miss ]
000000000000000000000000000
000
Tag
Offset
1
Index
4, 0 , 8, 36, 0
Miss
Hit
Result: Load from memory and place in Set 1 - Block 0
0
M[8]
1
M[12]
Miss

## Slide 21: 3. SA Cache Example: Load #4
 | Block 0 |  |  |  | Block 1 |  |  | 
Set Index | Valid | Tag | W0 | W1 | Valid | Tag | W0 | W1
0 | 1 | 0 | M[0] | M[4] | 0 |  |  | 
1 | 1 | 0 | M[8] | M[12] | 0 |  |  | 
Load from 36 
Check: [Valid but tag mismatch] Set 0 - Block 0 [Invalid] Set 0 - Block1 [ Cold Miss ]
000000000000000000000000010
100
Tag
Offset
0
Index
4, 0 , 8, 36, 0
Miss
Hit
Miss
Result: Load from memory and place in Set 0 - Block 1
2
M[32]
1
M[36]
Miss

## Slide 22: 3. SA Cache Example: Load #5
 | Block 0 |  |  |  | Block 1 |  |  | 
Set Idx | Valid | Tag | W0 | W1 | Valid | Tag | W0 | W1
0 | 1 | 0 | M[0] | M[4] | 1 | 2 | M[32] | M[36]
1 | 1 | 0 | M[8] | M[12] | 0 |  |  | 
Load from 0 
Check: [Valid and tags match] Set 0-Block 0 [Valid but tags mismatch] Set 0-Block1
[ Temporal Locality ]
000000000000000000000000000
000
Tag
Offset
0
Index
4, 0 , 8, 36, 0
Miss
Hit
Miss
Miss
Hit

## Slide 23: 4. Fully Associative (FA) Cache
Compulsory misses
  On the first access to a block; the block must be brought into the cache
  Also called cold start misses or first reference misses
Conflict misses
  Occur in the case of direct mapped cache or set associative cache, when several blocks are mapped to the same block/set
  Also called collision misses or interference misses
Capacity misses
  Occur when blocks are discarded from cache as cache cannot contain all blocks needed
Occurs in
Fully Associative Cache

## Slide 24: 4. Fully Associative (FA) Cache: Analogy
Let's not restrict the book by title any more. A book can go into any location on the desk!

## Slide 25: 4. Fully Associative (FA) Cache
Fully Associative Cache
  A memory block can be placed in any location in the cache
Key Idea:
  Memory block placement is no longer restricted by cache index or cache set index
  ++ Can be placed in any location, BUT
  --- Need to search all cache blocks for memory access

## Slide 26: 4. Fully Associative Cache: Mapping
Cache Block size = 2N bytes
Number of cache blocks = 2M
Offset = N bits
Tag = 32 – N bits
Cache Block size = 2N bytes
Memory Address
31
0
N-1
N
Block Number
Offset
31
0
N-1
Tag
Offset
Observation:
The block number serves as the tag in FA cache.
N

## Slide 27: 4. Fully Associative Cache: Circuitry
Example:
  4KB cache size and 16-Byte block size
  Compare tags and valid bit in parallel
No Conflict Miss (since data can go anywhere)
... ... ... … … … … …
0
1
2
3
254
255
Index
Valid
Tag
Bytes 0-3
Bytes 4-7
Bytes 8-11
Bytes 12-15
28-bit
4-bit
Tag
Offset
=
=
=
=
=
=

## Slide 28: 4. Cache Performance
Total Miss = Cold miss + Conflict miss + Capacity miss
Capacity miss (FA) = Total miss (FA) – Cold miss (FA), when Conflict Miss0
Identical block size
Observations:
Cold/compulsory miss remains the same irrespective of cache size/associativity.
For the same cache size, conflict miss goes down with increasing associativity.
Conflict miss is 0 for FA caches.
For the same cache size, capacity miss remains the same irrespective of associativity.
Capacity miss decreases with increasing cache size .

## Slide 29: 5. Block Replacement Policy (1/3)
Set Associative or Fully Associative Cache:
  Can choose where to place a memory block
  Potentially replacing another cache block if full
  Need block replacement policy
Least Recently Used (LRU)
  How: For cache hit, record the cache block that was accessed
    When replacing a block, choose one which has not been accessed for the longest time
  Why: Temporal locality

## Slide 30: 5. Block Replacement Policy (2/3)
Least Recently Used policy in action:
  4-way SA cache
  Memory accesses: 0 4 8 12 4 16 12 0 4
8
12
4
16
4
16
12
0
0
4
8
12
LRU
0
8
12
4
8
4
16
12
16
12
0
4
Hit
Miss (Evict Block 0)
Hit
Miss (Evict Block 8)
Hit
Access 4
Access 16
Access 12
Access 0
Access 4
x
x

## Slide 31: 5. Block Replacement Policy (3/3)
Drawback for LRU
  Hard to keep track if there are many choices
Other replacement policies:
  First in first out (FIFO)
  Random replacement (RR)
  Least frequently used (LFU)

## Slide 32: 6. Additional Examples #1
Direct-Mapped Cache:
  Four 8-byte blocks
Memory accesses: 4, 8, 36, 48, 68, 0, 32
Index | Valid | Tag | Word0 | Word1
0 | 0 |  |  | 
1 | 0 |  |  | 
2 | 0 |  |  | 
3 | 0 |  |  | 
Addr: Tag Index Offset
4: 00…000 00 100
8: 00…000 01 000
36: 00…001 00 100
48: 00…001 10 000
68: 00…010 00 100
0: 00…000 00 000
32: 00…001 00 000
M[0]
M[4]
0
1
M[8]
M[12]
0
1
M[48]
M[52]
1
1
M[32]
M[36]
1
M[64]
M[68]
2
M[0]
M[4]
0
M[32]
M[36]
1

## Slide 33: 6. Additional Examples #2

Addr: Tag Offset
4: 00…00000 100
8: 00…00001 000
36: 00…00100 100
48: 00…00110 000
68: 00…01000 100
0: 00…00000 000
32: 00…00100 000
Fully-Associative Cache:
  Four 8-byte blocks
  LRU Replacement Policy
Memory accesses: 4, 8, 36, 48, 68, 0, 32
Index | Valid | Tag | Word0 | Word1
0 | 0 |  |  | 
1 | 0 |  |  | 
2 | 0 |  |  | 
3 | 0 |  |  | 
M[0]
M[4]
0
1
M[8]
M[12]
1
1
M[32]
M[36]
4
1
M[48]
M[52]
6
1
M[64]
M[68]
8
M[0]
M[4]
0
Hit

## Slide 34: 6. Additional Examples #3

Addr: Tag Index Offset
4: 00…0000 0 100
8: 00…0000 1 000
36: 00…0010 0 100
48: 00…0011 0 000
68: 00…0100 0 100
0: 00…0000 0 000
32: 00…0010 0 000
 | Block 0 |  |  |  | Block 1 |  |  | 
Set Index | Valid | Tag | Word0 | Word1 | Valid | Tag | Word0 | Word1
0 | 0 |  |  |  | 0 |  |  | 
1 | 0 |  |  |  | 0 |  |  | 
2-way Set-Associative Cache:
  Four 8-byte blocks
  LRU Replacement Policy
Memory accesses: 4, 8, 36, 48, 68, 0, 32
M[0]
M[4]
0
1
M[8]
M[12]
0
1
M[32]
M[36]
2
1
M[48]
M[52]
3
M[64]
M[68]
4
M[0]
M[4]
0
M[32]
M[36]
2

## Slide 35: 7. Summary: Cache Organizations
One-way set associative
(direct mapped)
Block
Tag
Data
0
1
2
3
4
5
6
7
Two-way set associative
0
1
2
3
Set
Tag
Data
Tag
Data
0
1
Set
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Four-way set associative
Eight-way set associative (fully associative)
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data
Tag
Data

## Slide 36: 7. Summary: Cache Framework (1/2)
Block Placement: Where can a block be placed in cache?
Direct Mapped:
N-way Set-Associative:
Fully Associative:
Only one block defined by index
Any one of the N blocks within the set defined by index
Any cache block
Direct Mapped:
N-way Set Associative:
Fully Associative:
Tag match with only one block
Tag match for all the blocks within the set
Tag match for all the blocks within the cache
Block Identification: How is a block found if it is in the cache?

## Slide 37: 7. Summary: Cache Framework (2/2)
Block Replacement: Which block should be replaced on a cache miss?
Direct Mapped:
N-way Set-Associative:
Fully Associative:
No Choice
Based on replacement policy
Based on replacement policy
Write Strategy: What happens on a write?
  Write Policy: Write-through vs write-back
  Write Miss Policy: Write allocate vs write no allocate

## Slide 38: 8. Exploration: Improving Cache Penalty
So far, we tried to improve Miss Rate:
  Larger block size
  Larger Cache
  Higher Associativity
What about Miss Penalty?
Average Access Time
= Hit rate x Hit Time + (1-Hit rate) x Miss penalty

## Slide 39: 8. Exploration: Multilevel Cache
Options:
  Separate data and instruction caches, or a unified cache
Sample sizes:
  L1: 32KB, 32-byte block, 4-way set associative
  L2: 256KB, 128-byte block, 8-way associative
  L3: 4MB, 256-byte block, Direct mapped
Disk
Reg
L1 I$
L1 D$
Unified
L2 $
Memory
Processor

## Slide 40: 8. Exploration: Intel Processors
Itanium 2 McKinley
L1: 16KB I$ + 16KB D$
L2: 256KB
L3: 1.5MB – 9MB
Pentium 4 Extreme Edition
L1: 12KB I$ + 8KB D$
L2: 256KB
L3: 2MB

## Slide 41: 8. Exploration: Trend: Intel Core i7-3960K
Intel Core i7-3960K
per die:
2.27 billion transistors
15MB shared Inst/Data Cache (LLC)
per Core:
-32KB L1 Inst Cache
-32KB L1 Data Cache
-256KB L2 Inst/Data Cache
-up to 2.5MB LLC

## Slide 42: Reading
Large and Fast: Exploiting Memory Hierarchy
  Chapter 7 sections 7.1 – 7.2 (3rd edition)
  Chapter 5 sections 5.1 – 5.2 (4th edition)

## Slide 43: End of File