## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #24
Performance

## Slide 2: Lecture #24: Performance
Performance Definition
Factors Affecting Performance
Amdahl’s Law

## Slide 3: 1. Performance: Two Viewpoints
“Computer X is faster than computer Y” is an ambiguous statement
  “Fast” can be interpreted in different ways
Fast = Response Time
  The duration of a program execution is shorter
Fast = Throughput
  More work can be done in the same duration
We focus on the first viewpoint in this section

## Slide 4: 1. Execution Time: Comparison
Performance is in “units of things per second”
  Bigger is better
Response time is in “number of seconds”
  Smaller is better
Speedup n, between x and y is

## Slide 5: 1. Execution Time: Refining Definition
There are different measures of execution time in computer performance:
Elapsed time (aka wall-clock time)
  Counts everything (including disk and memory accesses, I/O, etc.)
  Not so good for comparison purposes
CPU time
  Doesn’t include I/O or time spent running other programs
  Can be broken up into system time and user time
Our focus: User CPU Time
  Time spent executing the lines of code in the program

## Slide 6: 1. Execution Time: Clock Cycles
Instead of reporting execution time in seconds, we often use clock cycles (basic time unit in machine).
Clock
Cycle time
Cycle time (or cycle period or clock period)
  Time between two consecutive rising edges, measured in seconds.
Clock rate (or clock frequency)
  = 1 / cycle-time
  = number-of-cycles/second (unit is Hz; 1 Hz = 1 cycle/second)

## Slide 7: 1. Execution Time: Version 1.0
Therefore, to improve performance (everything else being equal), you can do the following:
 Reduce the number of cycles for a program, or
 Reduce the clock cycle time, or equivalently,
 Increase the clock rate

## Slide 8: Exercise 1: Clock Cycle & Clock Rate
Program P runs in 10 seconds on machine A, which has a 400 MHz clock.
Suppose we are trying to build a new machine B that will run this program in 6 seconds. Unfortunately, the increase in clock rate has an averse effect on the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for the same program. What clock rate should we target at to hit our goal?

Answer:
  Let C be the number of clock cycles required for that program.
  For A: Time = 10 sec. = C  1/400MHz
  For B: Time = 6 sec. = (1.2  C)  1/clock_rateB
  Therefore, clock_rateB =
10  400  1.2/6 MHz
= 800 MHz

## Slide 9: 1. Clock Cycles: Proportional?
Each instruction takes n clock cycles
An execution consists of I number of instructions
Does it mean we need I  n cycles to finish it?
   Number of cycles is proportional to number of instructions?
1st instruction
2nd instruction
3rd instruction
4th
5th
6th
...
Clock

## Slide 10: 1. Clock Cycles: Inst Type Dependent
Different instructions take different amount of time to finish:
Clock
For example:
  Multiply instruction may take longer than an Add instruction.
  Floating-point operations take longer than integer operations.
  Accessing memory takes more time than accessing registers

## Slide 11: 1. Execution Time: Introducing CPI
A given program will require
  Some number of instructions (machine instructions)
 average Cycle per Instruction (CPI)
  Some number of cycles
 cycle time
  Some number of seconds
We use the average CPI as different instructions take different number of cycles to finish

## Slide 12: 1. Execution Time: Version 2.0
Average Cycle Per Instruction (CPI)
  CPI = (CPU time  Clock rate) / Instruction count
  = Clock cycles / Instruction count
CPU time = Seconds = Instructions x Cycles x Seconds
Program Program Instruction Cycle
where

## Slide 13: 2. Performance: Influencing Factors
Program compiles into Binary
Compiler
ISA
#instructions
Average CPI
Binary executes on Machine
Hardware Organization
Cycle Time
CPI
Process
Factors
Performance aspects influenced by factors

## Slide 14: 2. Program  Binary: Factors
Compiler:
  Different compilers may generate different binary codes
    e.g. gnu vs intel c/c++ compiler
  Different optimization may generate different binary codes
    e.g. different optimization level in gnu c compiler
Instruction Set Architecture:
  The same high level statement can be translated differently depending on the ISA
    e.g. same C program under Intel machine vs Sunfire server

## Slide 15: Exercise 2: Impact of Compiler

Given a program P, a compiler can generate 2 different binaries on a target machine. On that machine, there are 3 classes of instructions: Class A, Class B, and Class C, and they require 1, 2, and 3 cycles respectively.
First binary has 5 instructions: 2 of A, 1 of B, and 2 of C. Second binary has 6 instructions: 4 of A, 1 of B, and 1 of C.
Answer:
  Let T be the cycle time.
  Time(code1) = (21 + 12 + 23)  T = 10T
  Time(code2) = (41 + 12 + 13)  T = 9T
  Time(code1)/Time(code2) =
  CPI(code1) =
  CPI(code2) =
1. Which code is faster? By how much?
2. What is the (average) CPI for each code?
10/9 = 1.1
 Code2 is 1.1 times faster
(21 + 12 + 23) / (2 + 1 + 2) = 2
(41 + 12 + 13) / (4+ 1 + 1) = 1.5

## Slide 16: 2. Execution of Binary Code: Factors
Machine
  More accurately the hardware implementation
  Determine cycle time and cycle per instruction
Cycle Time:
  Different clock frequencies (e.g. 2GHz vs 3.6GHz)
Cycles Per Instruction:
  Design of internal mechanism (e.g. specific accelerator to improve floating point performance)

## Slide 17: Exercise 3: Impact of Machine

Suppose we have 2 implementations of the same ISA, and a program is run on these 2 machines.
Machine A has a clock cycle time of 10 ns and a CPI of 2.0. Machine B has a clock cycle time of 20 ns and a CPI of 1.2.
1. Which machine is faster for this program? By how much?
Answer:
  Let N be the number of instructions.
  Machine A: Time = N  2.0  10 ns
  Machine B: Time =
  Performance(A)/Performance(B) = Time(B)/Time(A)
  =
N  1.2  20 ns
(1.2  20) / (2.0  10) = 1.2

## Slide 18: Exercise 4: All Factors (1/4)
You are given 2 machine designs M1 and M2 for performance benchmarking. Both M1 and M2 have the same ISA, but different hardware implementations and compilers. Assuming that the clock cycle times for M1 and M2 are the same, performance study gives the following measurements for the 2 designs.
Instruction class | For M1 |  | For M2 | 
 | CPI | No. of instructions executed | CPI | No. of instructions executed
A | 1 | 3,000,000,000,000 | 2 | 2,700,000,000,000
B | 2 | 2,000,000,000,000 | 3 | 1,800,000,000,000
C | 3 | 2,000,000,000,000 | 3 | 1,800,000,000,000
D | 4 | 1,000,000,000,000 | 2 | 900,000,000,000

## Slide 19: Exercise 4: All Factors (2/4)

What is the CPI for each machine?
Let Y = 1,000,000,000,000
CPI(M1) = (3Y1 + 2Y2 + 2Y3 + Y4) / (3Y + 2Y + 2Y + Y) = 17Y / 8Y = 2.125
CPI(M2) = =
Which machine is faster? By how much?
Let C be cycle time.
Time(M1) = 2.125  (8Y  C) Time(M2) =
M1 is faster than M2 by
[(3Y2 + 2Y3 + 2Y3 + Y2)  0.9] / [(3Y + 2Y + 2Y + Y)  0.9]
20Y / 8Y = 2.5
2.5  (8Y  0.9  C) = 2.25  (8Y  C)
2.25 / 2.125 = 1.0588

## Slide 20: Exercise 4: All Factors (3/4)

To further improve the performance of the machines, a new compiler technique is introduced. The compiler can simply eliminate all class D instructions from the benchmark program without any side effects. (That is, there is no change to the number of class A, B and C instructions executed in the 2 machines.) With this new technique, which machine is faster? By how much?
Let Y = 1,000,000,000,000; Let C be cycle time.
CPI(M1) = (3Y1 + 2Y2 + 2Y3) / (3Y + 2Y + 2Y) = 13Y / 7Y = 1.857
CPI(M2) = =
Time(M1) = 1.857  (7Y  C)
Time(M2) =
M1 is faster than M2 by
[(3Y2 + 2Y3 + 2Y3)  0.9] / [(3Y + 2Y + 2Y)  0.9]
18Y / 7Y = 2.571
2.571  (0.9  7Y  C) = 2.314  (7Y  C)
2.314 / 1.857 = 1.246

## Slide 21: Exercise 4: All Factors (4/4)

Alternatively, to further improve the performance of the machines, a new hardware technique is introduced. The hardware can simply execute all class D instructions in zero times without any side effects. (There is still execution for class D instructions.) With this new technique, which machine is faster? By how much?
Let Y = 1,000,000,000,000; Let C be cycle time.
CPI(M1) = (3Y1 + 2Y2 + 2Y3 + Y0) / (3Y + 2Y + 2Y + Y) = 13Y / 8Y = 1.625
CPI(M2) = =
Time(M1) = 1.625  (8Y  C)
Time(M2) =
M1 is faster than M2 by
[(3Y2 + 2Y3 + 2Y3 + Y0)  0.9] / [(3Y + 2Y + 2Y + Y)  0.9]
18Y / 8Y = 2.25
2.25  (0.9  8Y  C) = 2.025  (8Y  C)
2.025 / 1.625 = 1.246

## Slide 22: Summary: Key Concepts
Performance is specific to a particular program on a specific machine
  Total execution time is a consistent summary of performance
For a given architecture, performance increase comes from:
  Increase in clock rate (without adverse CPI effects)
  Improvement in processor organization that lowers CPI
  Compiler enhancement that lowers CPI and/or instruction count
Pitfall: Expecting improvement in one aspect of a machine’s performance to affect the total performance.

## Slide 23: 3. Amdahl’s Law (1/3)
Pitfall: Expecting the improvement of one aspect of a machine to increase performance by an amount proportional to the size of the improvement.
Example:
  Suppose a program runs in 100 seconds on a machine, with multiply operations responsible for 80 seconds of this time. How much do we have to improve the speed of multiplication if we want the program to run 4 times faster?
  100 (total time) = 80 (for multiply) + UA (unaffected)
   UA = 20
  100/4 (new total time) =
  Speedup =
80/Speedup (for multiply) + UA
80/5 = 16


## Slide 24: 3. Amdahl’s Law (2/3)
Example (continued):
  How about making it 5 times faster?
  100 (total time) = 80 (for multiply) + UA (unaffected)
  100/5 (new total time) =
  Speedup =
80/Speedup (for multiply) + UA
80/0 = ??? (impossible!)

There is no way we can enhance multiply to achieve a fivefold increase in performance, if multiply accounts for only 80% of the workload.

## Slide 25: 3. Amdahl’s Law (3/3)
Amdahl’s law:
  Performance is limited to the non-speedup portion of the program
Execution time after improvement
  = Execution time of unaffected part + (Execution time of affected part / Speedup)
Corollary of Amdahl’s law:
  Optimize the common case first!

## Slide 26: Exercise 5: Amdahl’s Law

Suppose we enhance a machine making all floating-point instructions run five times faster. If the execution time of some benchmark before the floating-point enhancement is 12 seconds, what will the speedup be if half of the 12 seconds is spent executing floating-point instructions?
Time =
Speedup =
6 (UA) + 6 (fl-pt) / 5 = 7.2 sec.
12 / 7.2 = 1.67

## Slide 27: Exercise 6: Amdahl’s Law

We are looking for a benchmark to show off the new floating-point unit described in the previous example, and we want the overall benchmark to show a speedup of 3. One benchmark we are considering runs for 100 seconds with the old floating-point hardware. How much of the execution time would floating-point instructions have to account for in this program in order to yield our desired speedup on this benchmark?
Speedup =
Time_FI =
3 = 100 / (Time_fl / 5 + 100 – Time_fl)
83.33 sec.

## Slide 28: End of File