## Slide 1: NUMBER SYSTEMS SUPPLEMENTARY NOTES
Complement number systems

## Slide 2: COMPLEMENTS (1/3)
“Find the complement of a number” or “complement a number” is the short way of saying… “find the negated value in that complement system”.
For example, the two questions below are equivalent.
  [4-bit] Find/get the 1’s complement of 0110 (or, 1’s complement this value: 0110) Answer: 1001.
  [4-bit] If x is 01101s, what is -x in 1’s complement form? Answer: 10011s
So, “find the 1’s complement of 0110” is not asking for “how is 0110 represented in 1’s complement”. See next two slides for more examples.

## Slide 3: COMPLEMENTS (2/3)
Examples:
  [8-bit] Find the 1’s complement of 00000101 (or, What is the 1’s complement of 00000101?) Answer: 11111010
  [8-bit] Find the 1’s complement of 11001000 (or, What is the 1’s complement of 11001000?) Answer: 00110111
  [8-bit] Find 1012 in 1’s complement (or, How is 1012 represented in 1’s complement?) Answer: 000001011s
  [8-bit] Find -1012 in 1’s complement (or, How is -1012 represented in 1’s complement?) Answer: 111110101s
  [6-bit] Find the 2’s complement of 111000 (or, What is the 2’s complement of 111000?) Answer: 001000
  [6-bit] Find the 2’s complement of 000101 (or, What is the 2’s complement of 0000000101?) Answer: 111011

## Slide 4: COMPLEMENTS (3/3)
More examples:
  [8-bit] What is 710 in 2’s complement form? Answer: 00000111
  [8-bit] What is -710 in 2’s complement form? Answer: 11111001
  [10-bit] What is 1410 in 1’s complement form? Answer: (0000001110)1s
  [10-bit] What is -1410 in 2’s complement form? Answer: (1111110010)2s

## Slide 5: END