## Slide 1: CS2100
Tutorial #5
MIPS Processor:
Datapath and control
(Prepared by: Aaron Tan)

## Slide 2
Generating ALUControl Signal
Opcode | ALUop | Instruction Operation | Funct field | ALU action | ALU control
lw |  | load word |  | add | 
sw |  | store word |  | add | 
beq |  | branch equal |  | subtract | 
R-type |  | add |  | add | 
R-type |  | subtract |  | subtract | 
R-type |  | AND |  | AND | 
R-type |  | OR |  | OR | 
R-type |  | set on less than |  | set on less than | 
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR
Generation of 2-bit ALUop signal will be discussed later
00
00
01
10
10
10
10
10
xxxxxx
xxxxxx
xxxxxx
10 0000
10 0010
10 0101
10 0100
10 1010
0010
0010
0110
0010
0110
0001
0000
0111
Instruction Type | ALUop
lw / sw | 00
beq | 01
R-type | 10
From lecture slide:

## Slide 3
Design of ALU Control Unit (1/2)
Input: 6-bit Funct field and 2-bit ALUop
Output: 4-bit ALUcontrol
Find the simplified expressions
 | ALUop |  | Funct Field ( F[5:0] == Inst[5:0] ) |  |  |  |  |  | ALU control
 | MSB | LSB | F5 | F4 | F3 | F2 | F1 | F0 | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  | 
sub |  |  |  |  |  |  |  |  | 
and |  |  |  |  |  |  |  |  | 
or |  |  |  |  |  |  |  |  | 
slt |  |  |  |  |  |  |  |  | 
0
0
X
X
X
X
X
X
0 0 1 0
0
0
X
X
X
X
X
X
0 0 1 0
0
1
X
X
X
X
X
X
0 1 1 0
X
1
0
1
0
0
0
0
0
0 0 1 0
1
0
1
0
0
0
1
0
0 1 1 0
1
0
1
0
0
1
0
0
0 0 0 0
1
0
1
0
0
1
0
1
0 0 0 1
1
0
1
0
1
0
1
0
0 1 1 1
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
ALUcontrol3 = 0
ALUcontrol2 = ?
ALUop0 + ALUop1 F1
From lecture slide:

## Slide 4
Control Design: Outputs
 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
0
0
1
1
0
0
0
1
0
1
1
0
1
0
1
0
0
0
1
X
X
0
1
0
0
0
0
0
X
X
0
0
0
1
0
1
0
1
0
1
0
1
1
0
From lecture slide:

## Slide 5
0
1
0
1
0
1
1
0
beq $1, $3, 12
Q1(i)
000100 00001 00011 0000000000001100
If (R[rs]==R[rt]) PC=PC+4+BrAddr
Registers File |  |  |  | ALU |  | Data Memory | 
RR1 | RR2 | WR | WD | Opr1 | Opr2 | Address | Write Data
$1
$3
$3 or $0
[$1]-[$3] or
MEM([$1]-[$3]) (random)
[$1]
[$3]
[$1] – [$3]
[$3]
Next PC value = PC + 4
or (PC+4) + (12×4)
000100
00001
00011
00000 00000 001100
Opr1
Opr2
RegDest | 
RegWrite | 
ALUSrc | 
MemRead | 
MemWrite | 
MemToReg | 
Branch | 
ALUop | 
ALUcontrol | 
X
0
0
0
0
X
1
01
0110
0
0
0
1
X
X
Easy, just copy from tables in previous slides.
Red means the data is actually used.
Blue means the data is not used.

## Slide 6
0
1
0
1
0
1
1
0
lw $24, 0($15)
Q1(ii)
100011 01111 11000 0000000000000000
R[rt] = M[R[rs]+SignExtImm]
Registers File |  |  |  | ALU |  | Data Memory | 
RR1 | RR2 | WR | WD | Opr1 | Opr2 | Address | Write Data
RegDest | 
RegWrite | 
ALUSrc | 
MemRead | 
MemWrite | 
MemToReg | 
Branch | 
ALUop | 
ALUcontrol | 
$15
$24
$24
0
MEM([$15]+0)
[$15]
0
[$15]+0
[$24]
1
1
1
0
1
0
00
0010
Next PC value = PC + 4
100011
01111
11000
00000 00000 000000
Opr1
Opr2
1
1
0
0

## Slide 7
0
1
0
1
0
1
1
0
sub $25, $20, $5
Q1(iii)
000000 10100 00101 11001 00000 100010
R[rd] = R[rs] – R[rt]
Registers File |  |  |  | ALU |  | Data Memory | 
RR1 | RR2 | WR | WD | Opr1 | Opr2 | Address | Write Data
$20
$5
$25
[$20] – [$5]
[$20]
[$5]
[$20] – [$5]
[$5]
Next PC value = PC + 4
000000
10100
00101
11001
00000
100010
Opr1
Opr2
RegDest | 
RegWrite | 
ALUSrc | 
MemRead | 
MemWrite | 
MemToReg | 
Branch | 
ALUop | 
ALUcontrol | 
1
1
0
0
0
0
0
10
0110
1
0
0
0

## Slide 8
5
4
5
2
8
5
6
3
Critical Path Analysis
Sequence/Series
a
b
c
Duration = a + b + c
a
b
c
Parallel
Duration = max(a,b,c)
Critical path duration = 5 + 4 + 8 + 6 = 23

## Slide 9
0
1
0
1
0
1
1
0
Q2(a)
SUB instruction
Inst-Mem (400)
Reg.File (200)
Control (100)
MUX (ALUSrc)
(30)
ALU
(120)
MUX (MToR)
(30)
Reg.File
(200)
Not critical path
400+200+30+120+30+200 = 980ps
0
1
Inst-Mem
400ps
-------------
Adder
100ps
-------------
MUX
30ps
-------------
ALU
120ps
-------------
Reg-File
200ps
-------------
Data-Mem
350ps
-------------
Control/ALUControl
100ps
-------------
Lshft/signext/AND
20ps

## Slide 10
0
1
0
1
0
1
1
0
Q2(b)
LW instruction
Inst-Mem (400)
Reg.File (200)
Control (100)
ALU
(120)
MUX (MToR)
(30)
Reg.File
(200)
Not critical path
400+200+120+350+30+200 = 1300ps
Why is MUX (ALUSrc) not included this time?
DataMem
(350)
Inst-Mem
400ps
-------------
Adder
100ps
-------------
MUX
30ps
-------------
ALU
120ps
-------------
Reg-File
200ps
-------------
Data-Mem
350ps
-------------
Control/ALUControl
100ps
-------------
Lshft/signext/AND
20ps

## Slide 11
0
1
0
1
0
1
1
0
Q2(c)
BEQ instruction
Inst-Mem (400)
Reg.File (200)
Control (100)
ALU
(120)
AND
(20)
Not critical path
400+200+30+120+20+30 = 800ps
MUX (ALUSrc)
(30)
MUX (PCSrc)
(30)
How about the green path: PC  Adder  MUX (PCSrc)?
How about the purple path: Inst.Mem  SignExt  LeftShift  Adder  MUX(PCSrc)?
Inst-Mem
400ps
-------------
Adder
100ps
-------------
MUX
30ps
-------------
ALU
120ps
-------------
Reg-File
200ps
-------------
Data-Mem
350ps
-------------
Control/ALUControl
100ps
-------------
Lshft/signext/AND
20ps

## Slide 12
Preliminary ….. for next set of Qs
We will stick to (some) R-type, lw, sw and beq to keep things simple for this tutorial
#include <stdint.h> provides (some) bitwidth datatypes
  int8_t, int_16_t, int32_t, int64_t, uint8_t, uint_16_t, uint32_t, and uint64_t for signed 8, 16, 32, and 64 bit integers and unsigned 8, 16, 32, and 64 bit integers, respectively
  Otherwise, something like int can be of different bitwidths on different machines and compilers
Use #include <stdbool.h> for Booleans (i.e., 1 bit true/false)
Hardware description languages allow for arbitrary bitwidth (even parametrized ones) to be used
C (from the C11 standard onwards) provides “bit fields” (arbitrary bit widths) but only for structs and unions (See later)

## Slide 13
Q3(a) Write a C data structure and a function to describe the register file and its operations.
int32_t _rf[32];
void RegFile(uint5_t RR1,
uint5_t RR2,
uint5_t WR,
int32_t WD,
int32_t *RD1,
int32_t *RD2,
bool RegWrite) {
// Because we need to send out multiple outputs,
// we will use passing by pointers.
*RD1 = (RR1 > 0)?_rf[RR1]:0;
*RD2 = (RR2 > 0)?_rf[RR2]:0;
if (RegWrite && WR)
_rf[WR] = WD;
}
An array of integers to store the registers content. The index shall be the name (i.e., register number) of the register.
Since we need to return two outputs, we will need to pass them back via pointers.
We can use C’s conditional statement or if-then-else. Both are perfectly fine.
Make sure that register 0 returns 0.
Make sure that we never write to register 0. Actually, harmless coz you can never read the content back. Still, just for completeness.

## Slide 14
Q3(b) Write a C data structure and a function to describe the data memory and its operations.
int32_t data_memory[1073741824];
int32_t AccessDataMemory(uint32_t address,int32_t WrData,
bool MemRead, bool MemWrite)
{
// We can do a sanity check here. You can at most do one memory operation.
// Will assume that "error" raises hell.
if (MemRead && MemWrite) {
error("Cannot do both read and write at the same time.")
}
if (MemRead) {
return data_memory[address];
}
if (MemWrite) {
data_memory[address] = WrData;
return 0;
}
}
Ridiculous number but without introducing OS, we will just live with this for now.
Straightforward
Simple error checking

## Slide 15
Q4. Multiplexing.
#define MUX(N) \
int##N##_t mux##N (int##N##_t in0, \
int##N##_t in1, \
bool ctrl) \
{ \
if (ctrl) return in1; \
else return in0; \
}
Macro processing is kind of automated text processing of your source code before it is passed to the compiler. It is useful especially for shortening repetitive coding. Not just save space but also so that you only need to fix one piece of code instead of fixing all the repeated copies. In the repetition process, it can also allow the programmer to vary some parts of the repetition on a case by case basis.
Macro “MUX” defined with “N” as a parameter.
Token pasting: the token “uint” is pasted with the value of parameter N and then with “_t”
Token pasting: the token “mux” is pasted with the value of parameter N to form a new token
In macro, one line, one statement. If you want to span multiple lines, use “\” for continuation.

## Slide 16
Q4. Multiplexing.
#define MUX(N) \
int##N##_t mux##N (int##N##_t in0, \
int##N##_t in1, \
bool ctrl) \
{ \
if (ctrl) return in1; \
else return in0; \
}
Macro processing is kind of automated text processing of your source code before it is passed to the compiler. It is useful especially for shortening repetitive coding. Not just save space but also so that you only need to fix one piece of code instead of fixing all the repeated copies. In the repetition process, it can also allow the programmer to vary some parts of the repetition on a case by case basis.
Example:
MUX(8);
int8_t mux8(int8_t in0,
int8_t in1,
bool ctrl)
{
if (ctrl) return in1;
else return in0;
};

## Slide 17
Q5. Main control.
 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
0
0
1
1
0
0
0
1
0
1
1
0
1
0
1
0
0
0
1
X
X
0
1
0
0
0
0
0
X
X
0
0
0
1
0
1
Recall: Control Design – Outputs
0
1
0
1
1
0
0
1

## Slide 18
Q5. Main control.
(a) _RegDst
(b) _ALUSrc
(c) _MEMRead
(d) _ALUOp
if (!opcode) *_RegDst = 1;
else *_RegDst = 0;
if (!opcode || opcode == 4) *_ALUSrc = 0;
else *_ALUSrc = 1;
if (opcode == 0x23) *_MemRead = 1;
else *_MemRead = 0;
switch (opcode) {
case 0: *_ALUOp = 2;
case 0x23: // lw
case 0x2b: *_ALUOp = 0; // sw
case 0x4: *_ALUOp = 1; // beq
}
 | RegDst | ALUSrc | MemToReg | Reg Write | Mem Read | Mem Write | Branch | ALUop | 
 |  |  |  |  |  |  |  | op1 | op0
R-type | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
lw | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
sw | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0
beq | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 1
beq:opcode = 0x4
lw: opcode = 0x23
sw:opcode = 0x2b

## Slide 19
Q6. ALUcontrol.
uint4_t ALUControl(uint2_t _ALUOp, uint6_t _funct) {
if (_ALUOp == 2) { // R-type; need to decode funct
switch (_funct) {
case 0x20: return 2; // add
case 0x22: return 6; // sub
case 0x24: return 0; // and
case 0x25: return 1; // or
case 0x27: return 0xC; // nor
case 0x2a: return 7; // slt
default: } // raise an error
}
else { // non R-type
if (_ALUOp == 0)
return 2; // Ask ALU to add
if (_ALUOp == 1)
return 6; // Ask ALU to subtract
}
}
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR
 | ALUop | 
 | op1 | op0
R-type | 1 | 0
lw | 0 | 0
sw | 0 | 0
beq | 0 | 1

## Slide 20
Q7. ALU.
ALUcontrol | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | slt
1100 | NOR
int32_t ALU(int32_t in0, int32_t in1,
uint4_t ALUcontrol, bool *ALUiszero)
{
int32_t result;
switch (ALUcontrol) {
case 0: result = in0 & in1; break;
case 1: result = in0 | in1; break;
case 2: result = in0 + in1; break;
case 6: result = in0 - in1; break;
case 7: result = (int32_t)(in0 < in1); break;
case 12: result = ~(in0 | in1); break;
}
*ALUiszero = (result == 0);
return(result);
}
in1 may be rt or immed. But this is settled prior to invoking the ALU.
Our input parameters are signed, so we are doing signed comparison here.
We use the bitwise complement (NOT) of C. Cannot use logical NOT “!”
ALUiszero passed by pointer and is always set based on the result.

## Slide 21
Borrowed from the book, “Gulliver’s Travels” by Jonathan Swift
Fundamental disagreement on how to crack open one’s boiled egg – from small end or from the big end 
Terms Big-Endian and Little-Endian introduced to Computing by Danny Cohen
  Internet Engineering Note (Note 137), “On Holy Wars and a Plea for Peace”: https://www.ietf.org/rfc/ien/ien137.txt
Gulliver’s Travels is available for free as part of Project Gutenberg: https://www.gutenberg.org/ebooks/65473
  First time Big-Endian is mentioned is on page 45 in chapter 4
For Fun

## Slide 22
Opr1
Opr2
0
1
0
1
1
0
0
1
Tutors: A datapath diagram for your use.

## Slide 23
END OF FILE